## Slide 1: SWPPP TRAINING
Akron-Canton Airport
September 2021
Speakers – Tim Arendt and Mark Ervin of Gresham Smith

## Slide 2: Today’s Agenda
1. SWPPP Training – All Attendees
Training Presentation (25 minutes)

## Slide 3
STORMWATER POLLUTION PREVENTION PLAN

## Slide 4
Materials used in airport or tenant “industrial activities” and exposed to stormwater can pollute streams without control measures.
Stormwater Pollution Prevention Plan is a tool required by Ohio EPA to prevent contamination of the surface waters.
Fueling
Deicing
Material Handling
Sediment
Industrial Activities
Vehicle Washing

## Slide 5: Storm Water Pollution Prevention Plan (SWPPP)
Stormwater
  Rainfall, melting ice, and melting snow that:
  Infiltrates through pervious surfaces (soils, gravel, swales) or
  Runs off over impervious surfaces (concrete, asphalt, rooftops, compacted soil)
  Flows through sewers, ditches as a point source to surface waters
Pollution
Substance introduced to stormwater with potential for violating surface water quality standards.
Pollution Prevention
Environmentally sound and cost-effective way to control potential contamination near source.

## Slide 6: SWPPP Applicability and Purpose
SWPPP for Overall Airport and
Tenant Lease Areas
Identifies stormwater pollutants and pollutant generating activities
Establishes pollutant control measures
Defines inspections and documentation

## Slide 7: CAK NPDES Permit
Permit includes:
  Authorized stormwater outfalls
  Pollutant discharge limits
  Stormwater sampling/reporting requirements
  SWPPP requirements

## Slide 8: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 9: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 10: 1. CAK Pollution Prevention Team

## Slide 11: 1. CAK Pollution Prevention Team Roles and Responsibilities
PPT Leader (CAK)
Assign team roles
CAK Tenant Team Members
Understand SWPPP/share with staff
Coordinate with your other plans
Manage pollution prevention at your facility
Implement control measures
Assist with inspections
Address spills or emergencies
Report issues to CAK PPT leader
Provide guidance to your staff
Coordinate inspections, reporting, training
Update SWPPP when changes
Correspond with regulators
Lead resolution of identified issues
Coordinate with other plans

## Slide 12: 1. CAK Pollution Prevention Team Roles and Responsibilities
CAK Maintenance Team Members
CAK Operations Team Members
  Read SWPPP
  Provide maintenance of controls
  Coordinate with CAK PPT Leader on maintenance issues and status
  Address maintenance issues with pollutant generating activities
  Understand location and function of structural control measures
  Provide guidance to team members
Understand pollutants and pollutant generating activities
Understand location and function of structural control measures
Document observations and collected data per SWPPP forms
Address operational performance issues with controls
  Understand polluting activities
Read SWPPP
Provide routine inspections

## Slide 13: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 14
2. Facility
Drainage Map

## Slide 15: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 16: 3. Potential Pollutant Sources
Vehicle/Aircraft Fueling
Vehicle/Aircraft Maintenance
Material Handling and Storage
Vehicle/Aircraft Washing
Sediment from Construction
Aircraft/Runway Deicing

## Slide 17: 3. Potential Pollutant Sources – Non-Stormwater Discharges
Discharges defined as “non-stormwater” are prohibited, except:
Fire hydrant flushings
Potable water, including water line flushings
Air conditioning condensate
Irrigation water IF pesticides and herbicides have been applied per instruction
Pavement or building washwater IF no detergents are used and it contains no sediment, debris or oil.

## Slide 18: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 19: 4. Pollutant Control Measures / Best Management Practices
Best Management Practices (BMPs)
Measures to control to the generation and extent of pollutants in stormwater
Types:
  Source Reduction Measures: Steps to reduce amount of pollutants
  Example: Blending of higher amounts of water with Type 1 deicer
  Operational Controls: Procedures to minimize extent pollutant contaminant stormwater
  Example: Use of absorbent materials to pick up fuel spills
  Structure Controls: Physical devices to remove pollutants from stormwater
  Example: Sand filters for removal of sediment

## Slide 20: 4. Pollutant Control Measures / Best Management Practices
General Practices
Avoid exposure to stormwater
Designate areas for activities
Maintain areas in an orderly manner
Use dry cleaning techniques when possible (dry sweep)
No sweeping or washing into storm drains
Collected and dispose of washwater or discharge to the sanitary sewer

## Slide 21: 4. Pollutant Control Measures / Best Management Practices
Spill Management
  Maintain spill response materials in sensitive areas
  Inspect and replenish spill kits

## Slide 22: 4. Pollutant Control Measures / Best Management Practices
Routine Observations
Unlabeled Drum Materials Exposed to Stormwater

## Slide 23: 4. Pollutant Control Measures / Best Management Practices
Aircraft / Vehicle Maintenance
  Perform maintenance activities in designated areas
  Use drip pans or tarps to capture drips or leaks
  Drain all parts of fluids prior to disposal
  Maintain an organized inventory of materials
  Prevent apron or hangar floor wash water from entering storm drains
  Use dry cleanup methods

## Slide 24: 4. Pollutant Control Measures / Best Management Practices
Waste Management
  Keep containers/dumpsters closed
  Store away from storm water conveyances
  Provide liquid or hazardous wastes with secondary containment
  Scrap metal and old equipment must be clean before storing outside

## Slide 25: 4. Pollutant Control Measures / Best Management Practices
Deicing
Aircraft deicing only at South Deicing Pad
  North Pad could be used but not typical
  Can apply limited deicer to critical aircraft surfaces at gates for safe aircraft taxi to pads (typically engine cowlings).
    No wing, rear stabilizer, fuselage deicing
Urea deicer application to pavement limited to emergency use
Deicer treatment system
  Be aware of what it is not designed to treat (oils, fuels, paint)

## Slide 26: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 27: 5. Monitoring and Inspections
ROUTINE INSPECTIONS
Focus on areas with industrial activities
Pollutant generating activities
BMPs / controls
Discharges
Frequency at discretion of PPT leader – quarterly suggested
MONTHLY DEICING SEASON
Focus on areas where deicing occurs, deicer controls/treatment
Outfalls discharging flows from pavement/aircraft deicing areas
Observe stormwater for typical deicing features
  Odors
  Coloration (orange/green/black)
  Biofilm / slime
QUARTERLY – ALL OUTFALLS
Visual assessment of water
Align with NPDES sampling where applicable
Observe stormwater for:
  Odors
  Coloration
  Clarity
  Solids
  Sheen
  Foam
Formal inspections and documentation performed by CAK Operations / Environmental Staff
Tenants must routinely inspect their own pollutant generating activities

## Slide 28: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 29: 6. Employee Training
Yearly training (this session) required for CAK and tenant pollution prevention team members
PPT members should make recorded training sessions available to staff engaging in pollutant generating, control measure operations, and controls maintenance activities
Record attendance in SWPPP documentation

## Slide 30: CAK SWPPP
Key components:
  Pollution Prevention Team
  Facility Drainage Map
  Potential Pollutant Sources
  Pollutant Control Measures
  Monitoring and Inspections
  Employee Training
  Recordkeeping

## Slide 31: 7. Recordkeeping
Forms found in SWPPP Appendix
Spill Log (location, date, material spilled, amount, environmental impacts, mitigation measures taken)
Routine (Quarterly) Inspection of Activities and Controls
Quarterly Visual Inspection Form for Outfalls
Training Attendance
Annual NPDES Report